Use of Satellite Imagery for Spatial Pattern Analysis on Landuse Change

Qiming Zhou1 and Baolin Li2 and Alishir Kurban3

1. Department of Geography, Hong Kong Baptist University, Hong Kong
Kowloon Tong, Kowloon, Hong Kong

2. State Key Laboratory of Environment and Resources Information System
Institute of Geographical Sciences and Resources Research, Chinese Academy of Sciences
Beijing, 100101, P.R. China

3. Xinjiang Institute of Ecology and Geography, Chinese Academy of Sciences
40-3 South Beijing Road, Urumqi, Xinjiang 830011, China

# Abstract

This study attempts to develop a methodology to quantify spatial patterns of land cover change using landscape metrics. First, multi-temporal land cover types are derived based on a unified land cover classification scheme and from classification of multi-temporal remotely sensed imagery. Categorical land cover change trajectories are then established and reclassified according to the nature and driving forces of the change. Finally, spatial pattern metrics of the land cover change trajectory classes are computed and their relationships to human activities and environmental factors are analyzed. A case study shows that during the 30-year study period, the natural force is still dominant in environmental change, although the human impact through altering water resources and surface materials has increased dramatically in recent years. The human-induced change trajectories generally show lower normalized landscape shape index (NLSI), interspersion and juxtaposition index (IJI) and area-weighted mean patch fractal dimension (FARC_AM), indicating greater aggregation, fewer association with others and simpler and larger patches in shape, respectively. The results suggest that spatial pattern metrics of land cover change trajectories can provide a good quantitative measurement for better understanding on spatio-temporal pattern of land cover change due to different causes.

Keyword: multi-temporal image analysis, land cover change trajectory, change detection, landscape metrics, remote sensing, spatial pattern, aridzone.

# Introduction

Land cover change is one of the most sensitive indicators that echo the interactions between human activities and natural environment. In arid environment the land cover change often reflects the most significant impact on the environment due to human activities or natural forces. Remotely sensed data have been used for environment change study in decades and large collections of remote sensing imagery have made it possible to analyze changes of environmental elements and impact of human activities.

Change detection on land cover focuses mainly on four aspects: (1) detecting if a change has occurred, (2) identifying the nature of the change, (3) measuring the area extent of the change, and (4) assessing the spatial pattern of the change (MacLeod and Congalton, 1998).  Since spatial pattern of the change is shown as a good indicator of the impact by the other three aspects, its research has become quite active in change detection study (Narumalani et al., 2004; Nagendra et al., 2004).

One commonly used method to study the spatial pattern of land cover change is the bi-temporal profile method (Coppin et al. 2004). Using this method, multi-temporal satellite images were firstly classified into land cover classes on each acquisition date. Landscape metrics are subsequently computed to quantify spatial patterns shown by these land cover classes. The spatial pattern of land cover change on a ‘two-epoch’ timescale (i.e. the change between two dates) can then be described based on the comparison of these metrics (e.g. Dewidar, 2004; Tang et al., 2005).

With the accumulation of remotely sensed images over the past decades, it is now possible to analyze the spatial pattern of land cover change over a long period of time. Attempts have been made and reported on applications that extend the bi-temporal profile method to multiple epochs (e.g. Herold et al., 2003; McConnell et al., 2004). However, to understand causes of land cover changes, study often focuses on the metrics of land cover classes that form a part of input parameters together with other environmental or human factors. The spatial pattern of the change, which is measured by landscape metrics derived from multi-temporal classified images, is rarely analyzed.

Some recent research has developed methods of temporal trajectory analysis to trace paths of land cover change for given locations (e.g. Mertens and Lambin, 2000; Petit et al., 2001; Crews-Meyer, 2001; Liu and Zhou, 2004). Zhou et al. (2004) has reported a research that categorical trajectories of land cover change were established and classified according to the driving forces of the change, and pointed out the need of further study on the spatial pattern of such trajectories. Southworth et al. (2002) inferred the patterns of landuse change using landscape metrics of change trajectories. The landuse was classified into two classes, namely, forest and non-forest. Change trajectories (e.g. forest(forest(non-forest) were established based on three epochs, and the landscape metrics of them were then computed. This research focused on categorical change of a given landuse type (i.e. forest) rather than the comparison of different classes. Crews-Meyer (2004) assessed the temporal persistence of landuse and land cover through the analysis of ‘pixel-history’ of the pattern metrics of cover classes. Trajectory classes of pattern metrics (e.g. “decrease all three periods”, “decrease, stable, increase” and “decrease, increase, increase” for percentage of area – PCT) were derived. This study principally focused on the trajectories of metrics, rather than metrics of change trajectories. Further research is therefore needed to develop a methodology that quantifies the spatial pattern of change trajectories so that spatio-temporal pattern of the change can be better described and its relation to environmental and human factors may be further explored.

This study seeks an efficient and practical methodology to quantify spatial pattern of land cover change that can be related to both human activities and natural factors. The basic approach is to derive and interpret spatial pattern metrics of multi-epoch trajectories of land cover change. This method integrates multi-temporal and multi-scale remotely sensed data from various sources with a monitoring time frame of 30 years, including historical and state-of-the-art high-resolution satellite imagery. The history of land cover change for every location in the study area is traced, and nature, area extent and spatial pattern of such changes are also analyzed.

# Methodology

The approach of this study is based on post-classification comparison method, which is commonly employed in remote sensing change detection studies. Firstly, multi-temporal images are classified into land cover types for each acquisition date using a unified land cover classification scheme. Then, land cover change trajectories, or categorical ‘pixel history’, are established based on the classified images. The trajectories are then reclassified according to the nature of land cover changes. Finally, landscape metrics of the reclassified land cover change trajectories are computed and analyzed.

## Study area and data

The study area is centered at about 41(5’N and 85(43’E in Donghetan Township, Yuli County, Xinjiang Uygur Autonomous Region of China. It locates at the middle reach of Tarim River, the longest inland river of China (Figure 1). At the fringe of Taklimakan Desert, the “green corridor” of Tarim Basin is one of the most important habitation areas in aridzone of China. The landscape in Donghetan is typical in China’s aridzone, with a generally dry and harsh environment, represented by typical desert vegetation and soils. With the increasing land development in recent decades, the fragile environment has experienced quite remarkable change, largely reflecting the general development trend and temporal effects of government policies and administrative measures.

Figure 1. Location map of the study area.

Five multi-temporal remotely sensed images were acquired for change detection of this study, including Landsat MSS (3/7/1973, 12/10/1976), TM (25/9/1994), ETM (17/9/2000) and SPOT HRV (20/7/1986) multi-spectral images. In addition, a multi-spectral 4-m resolution IKONOS image was also acquired in September 2000 to assist in field investigations and accuracy assessment of the image classification. The IKONOS image was geo-referenced to a 1:10,000 map using 22 Ground Control Points (GCPs). The other images were then geometrically corrected and registered on the map coordinates using image-to-image registration to the master IKONOS image. Efforts were made to control registration errors to within half a pixel of the image concerned, so that the errors caused by mis-registration would be less critical.

## Classification

To minimize seasonal impacts of remotely sensed data, the post-classification comparison method was employed for image processing, since this method is less sensitive to radiometric variations between the scenes (Mas, 1999). Supervised classification was employed to classify individual images independently, using a unified land cover classification scheme to ensure that the classifications of the multi-scale, multi-temporal images are compatible with each other (Table 1). Images were classified into the Level 2 classes, which were subsequently merged into the five unified classes.

Table 1. Unified land cover classification scheme for multi-scale, multi-temporal images. The numbers denote the land-use class code in individual classifications.

| Level 1 classes | Level 2 classes | ETM (2000) | TM (1994) | SPOT (1986) | MSS (1976) | MSS (1973) | Unified classes |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cropland | Cropland | 1 | 1 | - | - | - | Cropland (1) |
| Grass and woodland | Dense grass and woodland | 2 | 2 | 2 | 2 | 2 | Grass and woodland (2) |
|  | Sparse grass and woodland | 3 | 3 | 3 | 3 | 3 |  |
|  | Mowing land | 4 | - | - | - | - |  |
|  | Salty grass | 5 | 5 | 5 | 5 | 5 | Salty grass (3) |
| Water body | Ponds | 6 | 6 | 6 | 6 | 6 | Water body (4) |
|  | River | 7 | 7 | 7 |  |  |  |
| Unused land | Bare ground and sand dunes | 8 | 8 | 8 | 8 | 8 | Bare ground (5) |

## Post-classification processing

Spatial resolution of images affects landscape metric computation greatly (Borak et al., 2000; Rocchini, 2005). To make the classified land cover images comparable in terms of landscape metric, the images must have the same spatial resolution. Our approach is to resample the classified images to the lowest spatial resolution of all images and the majority rule aggregation is used for the resampling, as the method that Petit and Lambin (2001) proposed.

After resampling, a majority filter was applied to the classified images for the removal of isolated pixels to minimize potential analytical errors.

## Accuracy assessment

In this study we have chosen stratified random sampling scheme for selecting sample points of reference data for classification accuracy assessment. 790 sample points were selected and input to a GIS. They were then overlaid with the classified images as well as the high-resolution IKONOS multi-spectral image.

Collecting reference data for accuracy assessment on multi-temporal images always presents a serious constrain, because simultaneous ‘ground truthing’ data over a long period of time are very difficult, if not impossible, to find. In this study, we could only acquire a high-resolution IKONOS multi-spectral image that was simultaneous with the 2000 ETM data. Although the IKONOS image has a high enough resolution for ‘ground truthing’, the ‘time gaps’ between this ‘reference image’ and some historical images are large.

In this study, we used the IKONOS image as the source of the reference data to assess the results of the 2000 ETM classifications. For the other four historical images, we used the IKONOS image as the basis for comparison for proper interpretation. By this means, obvious land cover changes such as grasslands to water and bare ground to cropland could be reliably detected by image interpretation. Field visits and interviews to elderly locals were also conducted for sample points where a clear relationship between the present and historical images could not be established.

## Establishment and reclassification of land cover change trajectories

The concept and methodology of land cover change trajectory has been developed (Mertens and Lambin, 2000; Petit et al., 2001; Crews-Meyer, 2001; Zhou et al., 2004). In this study the term trajectory of land cover change refers to successions of land cover types for a given sample unit over more than two observations (epochs).

To establish land cover change trajectories, all classified images were integrated in GIS using raster format with ARC/INFO GIS software. Based on the classification scheme as shown in table 1, all possible land cover change trajectories were established and then reclassified into ten classes including four unchanged classes, three classes of human induced change and three classes of changes by natural causes. The trajectory classification scheme is shown in table 2.

Table 2. Classification of landuse change trajectories.

| Level 1 classes | Level 2 classes | Description | Trajectory examples |
| --- | --- | --- | --- |
| Unchanged | Grass/woodland | No change* | G(G(G(G(G |
|  | Salty grass | No change* | S(S(S(S(S |
|  | Water body | No change* | W(W(W(W(W |
|  | Bare ground | No change* | B(B(B(B(B |
| Human-induced | Old cultivation | Changed to and remained as cropland since 1994 | G(G(G(C(C |
|  | New cultivation | Changed to and remained as cropland since 2000 | S(S(G(G(C |
|  | Reservoirs/ponds | Changed to and remained as water bodies since 1986 | G(G(W(W(W |
| Natural | Grass/woodland | Periodical changes between cover G and S | G(S(G(G(S |
|  | Flooded | Periodical changes between cover W and other types | G(W(G(W(G |
|  | Bare ground | Periodical changes between cover B and other types | G(B(B(G(B |

* Some ambiguous cases are also included considering that possible classification error may create once-only false class in the trajectory.

## Computation of landscape metrics

The computation of landscape metrics of land cover change trajectories was conducted using the FRAGSTATS, a program designed to compute a wide variety of landscape metrics for categorical map patterns (McGarigal and Marks, 1995; McGarigal et al., 2002). In this study, since land cover change trajectories are reclassified into ten classes, only class-level metrics would apply. Four landscape metrics that are commonly used in ecological studies and supported by FRAGSTATS are used in this study, namely, Percentage of Landscape (PLAND), Normalized Landscape Shape Index (NLSI), Interspersion and Juxtaposition Index (IJI) and Area-weighted Mean Patch Fractal Dimension (FARC_AM). The definition and meaning of these metrics are listed in table 3.

Table 3. Landscape metrics for analyzing spatial patterns of land cover change trajectories (retrieved from McGarigal et al., 2002).

| Abbreviation | Name | Equation* | Interpretation |
| --- | --- | --- | --- |
| PLAND | Percentage of Landscape |  | A measure of proportional abundance of each class in the area, ranging form 0 to 100. PLAND ( 0 when class i becomes increasingly rare, while PLAND = 100 when the entire area consists of a single class. |
| NLSI | Normalized Landscape Shape Index |  | A measure of class aggregation, ranging from 0 to 1. NLSI = 0 when the area consists of a single square or maximally compact patch of the class; NLSI increases as the class becomes increasingly disaggregated. |
| IJI | Interspersion and Juxtaposition Index |  | A measure of interspersion over the maximum possible interspersion for the given number of classes, ranging from 0 to 100. IJI ( 0 when the class is adjacent to only one of the other classes. IJI = 100 when the class is equally adjacent to all other classes (i.e., maximally interspersed and juxtaposed to other classes). |
| FARC_AM | Area Weighted Fractal Dimension Index |  | A measure of complexity of the shapes of class boundaries, ranging from 1 to 2. It uses class area as a weighting factor. FRAC_AM ( 1 for shapes with very simple perimeters such as squares, and . FRAC_AM ( 2 for shapes with highly convoluted, plane-filling perimeters. |

* where: i is the class of interest; j is the patch number of class i; Pi =  proportion of the landscape occupied by class i; aij = area (m2) of patch ij; A = total landscape area (m2); ei = total length of edge (or perimeter) of class i in terms of number of cell surfaces (including all landscape boundary and background edge segments involving class i); min ei = minimum total length of edge (or perimeter) of class i in terms of number of cell surfaces; max ei = maximum total length of edge (or perimeter) of class i in terms of number of cell surfaces; eik = total length (m) of edge in landscape between classes i and k; m = number of classes present in the landscape, including the landscape border, if present; pij =  perimeter (m) of patch ij.

# Results and discussion

## Image classification

The classification results are shown in figure 2 and overall accuracies of the classification are summarized in table 4.

Figure 2. Land cover classification (1973 – 2000).

Table 4. Overall accuracy assessment on the classification results

| Accuracy measures | 1973 | 1976 | 1986 | 1994 | 2000 |
| --- | --- | --- | --- | --- | --- |
| Original | Overall accuracy (%) | 88.9 | 85.8 | 88.9 | 89.8 | 87.1 |
|  | Kappa | 0.73 | 0.66 | 0.79 | 0.83 | 0.78 |
| Resampled | Overall accuracy (%) | 86.5 | 85.2 | 83.7 | 86.3 | 81.5 |
|  | Kappa | 0.68 | 0.63 | 0.67 | 0.77 | 0.68 |

From table 4 it can be seen that the image classification accuracy is to some extent influenced by image resampling, showing that the accuracy with original spatial resolution is higher than that with resampled pixels. This is clearly shown in the results from SPOT, TM and ETM images. When original pixels are resampled to a much lower spatial resolution (20(50m for SPOT, 30(50m for TM and ETM), the overall accuracy is reduced by 5.2%, 3.5% and 5.6% for 1986 (SPOT), 1994 (TM) and 2000 (ETM) images, respectively. The kappa coefficient also displays the same impact (0.79(0.67, 0.83(0.77, 0.78(0.68 for 1986, 1994, 2000 images, respectively). For the purpose of this study, the classification yields a satisfactory, though not ideal, result. Even after resampling, the classification still achieved accuracy around 85%, with kappa ranging from 0.63 to 0.77.

## Area change based on multi-temporal trajectory

Figure 3 shows the land cover change trajectory classification. In figure 3, land cover change trajectories are classified according to whether a categorical change occurred during the study period, and the cause of the change if happened. Based on figure 3 and bi-temporal profile of land cover change, table 5 summarizes the area change of land cover classes during the study period. From 1994 to 2000, cropland increased from 3.7% to 12.3% of the total area reflecting a three-fold increase in 6 years. The trajectory analysis result also shows that increasing cropland largely came from salty grass (5.2% in 1986 ( 2.9% in 2000) and water body (16.1% in 1986 ( 8.0% in 2000), indicating that most new cultivations were located in the river flat. Another significant human impact was the construction of a dam in the north of the study area in early 1980s, resulting in flooding of vast area of grass/woodlands, which decreased from 74.4% (1976) to 69.7% (1986) in area. In contrast, water body area increased from 8.4% to 16.1%.

Figure 3. The trajectory classification of land cover change from 1973 to 2000.

Table 5. Area change of land cover types from 1973 to 2000

|  | 1973 | 1976 | 1986 | 1994 | 2000 |
| --- | --- | --- | --- | --- | --- |
| Cropland | - | - | - | 229.3 | 773.8 |
|  | - | - | - | 3.7 | 12.3 |
| Grass and woodland | 4672.0 | 4635.0 | 4315.5 | 3881.3 | 4211.3 |
|  | 74.4 | 73.8 | 68.7 | 61.8 | 67.1 |
| Salty grass | 326.0 | 400.5 | 259.5 | 184.0 | 149.8 |
|  | 5.2 | 6.4 | 4.1 | 2.9 | 2.4 |
| Water body | 499.3 | 528.8 | 1011.8 | 1370.8 | 503.5 |
|  | 7.9 | 8.4 | 16.1 | 21.8 | 8.0 |
| Bare ground | 783.3 | 716.3 | 693.8 | 615.3 | 642.3 |
|  | 12.5 | 11.4 | 11.0 | 9.8 | 10.2 |

The impact from natural factors is also significant on land cover change. For example, water body increased from 8.4% (1976) to 18.0% (1986) and 21.8% (1994), and decreased to 8.0% - back to the same level of 1976. Although the construction of the dam in the north contributed largely to this fluctuation, the natural seasonal flooding may play even more important role. For other native land cover types, the up-and-down changes are also observed suggesting the reversible nature of the change caused by natural factors.

## Spatial pattern of land cover change trajectories

Table 6 shows the computation results of spatial pattern metrics of land cover change trajectory. The table illustrates the computation results at both Level 1 and Level 2 classes of change trajectories. As the purpose of this study is to assess human impact on the natural environment, cultivation classes are also merged for computation of the metrics.

Table 6. Spatial pattern metrics of land cover change trajectories.

| Level 1 classes | Level 2 classes | PLAND (%) | NLSI | IJI | FRAC_AM |
| --- | --- | --- | --- | --- | --- |
| Unchanged | Grass/woodland | 34.4 | 0.161 | 57.9 | 1.229 |
|  | Salty grass | 0.1 | 0.302 | 0.0 | 1.083 |
|  | Water body | 0.6 | 0.235 | 31.4 | 1.048 |
|  | Bare ground | 6.5 | 0.131 | 26.1 | 1.146 |
|  | All unchanged | 41.6 | 0.161 | 58.8 | 1.238 |
| Human-induced | Old cultivation | 2.1 | 0.226 | 50.7 | 1.074 |
|  | New cultivation | 10.6 | 0.137 | 61.2 | 1.120 |
|  | Reservoirs/ponds | 4.3 | 0.159 | 30.5 | 1.132 |
|  | All cultivation | 12.7 | 0.109 | 51.3 | 1.116 |
|  | All human-induced | 17.0 | 0.127 | 97.9 | 1.120 |
| Natural | Grass/woodland | 6.5 | 0.250 | 61.5 | 1.127 |
|  | Flooded | 28.7 | 0.191 | 62.7 | 1.168 |
|  | Bare ground | 6.2 | 0.387 | 59.5 | 1.130 |
|  | All natural | 41.4 | 0.173 | 69.9 | 1.239 |

The percentage of landscape (PLAND) shows the abundance of individual land cover change trajectory class. During the 30-year study period, the PLAND of unchanged area was 41.6%, compared with that of human-induced changes (17.0%) and change by natural factors (41.4%). For unchanged area, the PLAND of grass/woodland constitutes 80.3%, and for human-induced change, the PLAND of new cultivation reached 60.8%. For the categories of natural change, flooded area obviously dominates, with a PLAND of 64.3%. Given the fact that the study area is quite remote and human activities appear to be quite limited, it is understandable that most of environmental change is due to natural forces (e.g. flooding) rather than human activities. However, it should also be noted that PLAND of new cultivation accounts for 10.6%, which reveals the significant acceleration of land conversion to croplands in recent years, when human impact started to play an important role on the environmental change by altering the natural courses of water and surface materials.

Measured by Normalized Landscape Shape Index (NLSI), different change trajectory classes have demonstrated some clear differences in spatial aggregation. The human-induced change trajectories generally show larger class aggregation. NLSI of all human-induced classes is 0.127, which is the minimum among all three Level 1 classes. The NLSI of cultivation classes has shown significant change in landuse pattern. The ‘old cultivation’ has a NLSI of 0.226, similar to those of other natural classes. This indicates that cultivation style was still remaining as ‘self-supporting’ stage for individual farmers, who did not apply great impact on the natural environment. In contrast, the NLSI of ‘new cultivation’ is 0.137, which is much less than that of ‘old cultivation’, suggesting a larger-scale, commercial profit-oriented agricultural development, which made large impact on the environment by introducing large machinery, massive irrigation constructions and other modern agriculture input. When merging both ‘old’ and ‘new’ cultivation classes together, the aggregated NLSI is only 0.109, significantly less than all other natural classes. This confirms that recent cultivation exhibited a highly concentrated and aggregated spatial pattern with simple large patches for the efficiency of landuse.

The Interspersion and Juxtaposition Index (IJI) describes how a trajectory class spatially associates with other classes. Naturally the unchanged trajectory classes show lower IJI (i.e. spatially adjacent to fewer other trajectory classes) since a given change trajectory class tends to associate with its corresponding cover type (e.g. unchanged bare ground, or sand dunes, tends to be surrounded by periodical changes between cover bare ground and other cover types). Human-induced change generally shows lower IJI compared to natural change trajectory classes. Spatially the cultivation classes shows tendency to be associated with each other, shown by the IJI of all cultivation of 51.3, which is much less than that of natural trajectory classes (IJI = 69.9). The reservoirs/ponds trajectory class has shown a strong tendency to associate with unchanged water bodies and flooding zones (i.e. the ‘flooded’ natural change trajectory) with a low IJI of 30.5. In comparison, the natural change trajectories are more likely interspersed with other change trajectory classes because they often represent the interchange zone between different natural land cover types and areas with human impact.

Human-induced change has lower shape complexity measured by Area Weighted Fractal Dimension Index (FRAC_AM). For all Level 1 classes, human-induced change has the lowest FRAC_AM of 1.120, compared to those of unchanged (1.238) and natural (1.239) change trajectories. For cultivation trajectory classes, the new cultivation (FRAC_AM = 1.120) has more complex shape than that of old cultivation (FRAC_AM = 1.074), suggesting that cropland in 2000 was expanded around old cultivation fields. The boundaries of the expanded cropland in 2000 were more complex because of the appearances of holes occupied by the 1994 cropland patches. Actually, the change of shape complexity of old and new cultivation suggests the spatial pattern of cropland expansion: the originally scattered small patches of farmland found in 1994 were expanded to larger area, and new cultivation is unlikely to occur in isolated new area because of limited support of irrigation infrastructure.

# Conclusion

Land cover change in aridzone is caused by both human activities and natural forces. Sometimes natural factors have much larger impact than that of human activities. To effectively estimate and describe the dominance and spatial distribution of the forces that caused environmental change, we have proposed a methodology that uses multi-temporal remotely sensed imagery to derive land cover change trajectory, and subsequently computes landscape metrics of the change trajectory as quantitative descriptive parameters.

This research has selected four landscape metric measures to describe spatial pattern of land cover change trajectory classes in the study area of aridzone in western China. The findings of the case study can be summarized as:

- PLAND of change trajectory classes is a good indicator to show the dominant process of the environmental change. In the study area, the dominant process of environmental change was still due to natural forces, but the impact of human activities has increased significantly in recent years.

- Aggregation of patches of land cover change trajectory classes shows the nature of change processes. Larger aggregation often suggests more aggressive progress from a dominant driving force. In this study, the human induced changes generally show larger aggregation, indicated by lower NLSI, suggesting that human impact is more concentrated than the changes caused by natural forces.

- Among human-induced changes, the reservoirs/ponds class was closely associated with only few of the other change trajectory classes (e.g. flooding zones), indicated by its low IJI. The cultivation classes also show low IJI with the tendency of associating with each other.

- The whole human-induced trajectory class shows a lower FRAC_AM than those of natural changes, indicating less complexity in shape. This suggests that large, relatively regularly shaped patches are the general spatial pattern when lands were converted from natural cover types to cultivated lands or reservoirs. The comparison between the FRAC_AM of old and new cultivation also suggests that expansion of old cultivation was likely the representative process of farmland growth in the study area.

This study extends previous research reported by Southworth et al. (2002) and Crews-Meyer (2004) based on categorical trajectory analysis (Zhou et al., 2004). The landscape metric measurements have been introduced to analyze the spatial pattern of land cover change trajectory classes based on the driving force of environmental change. Taking this approach, the nature of change trajectories (hence the history of the change) can be described by interpreting the metrics of the spatial patches of change trajectories, thus to form a useful foundation for the prediction of spatial pattern of land cover change with the current driving forces and constrains.

Numerous challenges, however, are also raised from this study. First, similar to all other remote sensing studies, the uncertainty in classification and change detection based on multi-temporal and multi-resolution remotely sensed images will always produce significant impact on the analytical results. To what extent that the impact may affect the final analytical results is certainly subject to further study. Secondly, the interactions and associations among different land cover change trajectories need to be further explored by introducing other landscape metrics or other spatial pattern measures. The development of more comprehensive and representative parameters to describe spatio-temporal patterns and process shown by remotely sensed data is also recommended.

# Acknowledgements

The research is supported by National Key Basic Research and Development Program (2006CB701304), Research Grants Council Competitive Earmarked Research Grant (HKBU 2026/04P), and Hong Kong Baptist University Faculty Research Grant (FRG/03-04/II-66). The authors would like to thank the staff of Xinjiang Institute of Ecology and Geography, Chinese Academy of Sciences for their support during the fieldwork.

# References

Borak, J.S., Lambin, W.F. and Strahler, A.H., 2000, The use of temporal metrics for land cover change detection at coarse spatial scales. International Journal of Remote Sensing, 21(6-7), 1415-1432.

Coppin, P., Jonckheere, I., Nackaerts, K., Muys, B., and Lambin, 2004, Digital change detection methods in ecosystem monitoring: a review. International Journal of Remote Sensing, 25(9), 1565–1596.

Crews-Meyer, K.A., 2001, Assessing landscape change and population-environment interactions via panel analysis. Geocarto International, 16, 69-79.

Crews-Meyer, K.A., 2004, Agricultural landscape change and stability in northeast Thailand: historical patch-level analysis. Agriculture, Ecosystems and Environment, 101, 155–169.

Dewidar, K.H.M., 2004. Detection of land cover/land cover changes for the northern part of the Nile delta (Burullus region), Egypt. International Journal of Remote Sensing, 25(20), 4079–4089.

Herold, M., Goldstein, N.C., Clarke, K.C., 2003. The spatiotemporal form of urban growth: Measurement, analysis and modelling. Remote Sensing of Environment, 86, 286-302.

Liu, H., and Zhou, Q., 2004, Accuracy analysis of remote sensing change detection by rule-based rationality evaluation with post-classification comparison. International Journal of Remote Sensing, 25, 1037–1050.

MacLeod, R.D. and Congalton, R.G., 1998. A quantitative comparison of change-detection algorithms for monitoring eelgrass from remotely sensed data. Photogrammetric Engineering & Remote Sensing, 64(3), 207-216.

Mas, J.F., 1999, Monitoring land-cover changes: a comparison of change detection techniques. International Journal of Remote Sensing, 20(1): 139-152.

McConnell, W., Sweeney, S.P. and Mulley, B., 2004. Physical and social access to land: spatio-temporal patterns of agricultural expansion in Madagascar. Agriculture, Ecosystems and Environment, 101, 171–184.

McGarigal, K., and Marks, B.J., 1995, FRAGSTATS: spatial pattern analysis program for quantifying landscape structure. USDA Forest Service General Technical Report, PNW-351.

McGarigal, K., Cushman, S.A., Neel, M.C. and Ene, E., 2002. FRAGSTATS: Spatial Pattern Analysis Program for Categorical Maps. Computer software program produced by the authors at the University of Massachusetts, Amherst. Available at the following web site: www.umass.edu/landeco/research/fragstats/fragstats.html.

Mertens, B. and Lambin, E.F., 2000, Land-cover-change trajectories in southern Cameroon. Annals of the Association of American Geographers, 90, 467-494.

Nagendra, H., Munroe, D.K., Southworth, J., 2004. From pattern to process: landscape fragmentation and the analysis of land cover/land cover change. Agriculture, Ecosystems and Environment, 101, 111–115.

Narumalani, S., Mishra, D.R., Rothwell, R.G., 2004, Change detection and landscape metrics for inferring anthropogenic processes in the greater EFMO area. Remote Sensing of Environment, 91(3-4), 478-489.

Petit, C.C. and Lambin, E.F., 2001, Integration of multi-source remote sensing data for land cover change detection. International Journal of Remote Sensing, 15(8), 785-803.

Petit, C.C., Scudder, T. and Lambin, E.F., 2001, Quantifying processes of land-cover change by remote sensing: resettlement and rapid land-cover changes in south-eastern Zambia. International Journal of Remote Sensing, 22, 3435-3456.

Rocchini, D., 2005, Resolution problems in calculating landscape metrics. Spatial Science, 50(2), 25-35.

Southworth, J., Nagendra, H. and Tucker, C., 2002, Fragmentation of a landscape: Incorporating landscape metrics into satellite analyses of land-cover change. Landscape Research, 27(3), 253-269.

Tang, J., Wang, L. and Zhang, S., 2005. Investigating landscape pattern and its dynamics in Daqing, China. International Journal of Remote Sensing, 26(11), 2259–2280.

Zhou, Q., Li, B. and Zhou, C., 2004. Studying spatio-temporal pattern of landuse change in arid environment of China, In Advances in Spatial Analysis and Decision Making, Li, Z., Zhou, Q. and Kainz, W. (eds.), Swets & Zeitlinger, Lisse: 189-200.